## Slide 1
Assembling
Vermont’s
Intersection
Data
GIS-T 2019
Kerry Alley
Notes: Today I’ll be talking about our new Intersection Data

## Slide 2
  Data Creation – Maintenance – Use – Evolution
Interconnected Processes
Notes: Creating the VTrans Intersection Data required consideration of it’s use, maintenance, and potential changes in how intersections are modeled. Maintenance workflows, tools, new uses already exist and the data is not yet complete.

## Slide 3: Today’s Presentation
Our objectives/approach to Intersection Data
Internally developed automated processes
    (facilitating data creation
    and maintenance)
Future directions
Notes: I’ll be focusing on a subset of objectives that I haven’t heard as much about as I hang out with other intersection folks, and ideas that were particularly useful to us.
Farmed out tasks
    (not everything can be automated)

## Slide 4
MIRE and Safety Analyst compatible
Extensible and flexible
Requires little change in ongoing data maintenance efforts
Leverages existing data
Facilitates Agency-wide data integration
VTrans Objectives/Approach

## Slide 5
Intersection data capable of supporting intersection complexity and a generalized representation as needed, depending on use scenario
    Major and Minor Routes AND Individual Legs, Complex geometry
VTrans Objectives/Approach

## Slide 6
Intersection data capable of supporting intersection complexity and a generalized representation as needed, depending on use scenario
    Major and Minor Routes OR Legs, Complex geometry
Intersection features “wedded” to Road Centerline
    Approach (Leg) attributes extracted/updated from road centerline attributes
    Relationships between features indicated by
        Intersecting geometry
        Unique IDs shared between related features
VTrans Objectives/Approach

## Slide 7
Nodes
    Point features
NodeLegs
    Line features
Two Intersection Feature Classes
Node
NodeLeg
Nodes
&
NodeLegs
Notes: Before I talk about representing different scales of intersection complexity… Introduce you to our data, as I’ll be referring to these features a lot by name in the coming slides

## Slide 8
VTrans Objectives/Approach
●
Generalized Intersection
Intersection Complexity

## Slide 9
VTrans Objectives/Approach
●
Generalized!
HOW?

## Slide 10
One Node is the Principal Node
A subset of the NodeLegs are Principal NodeLegs
VTrans Objectives/Approach
Nodes
NodeLegs
Road Centerline
Complex Intersection

## Slide 11
One Node is the Principal Node
A subset of the NodeLegs are Principal NodeLegs
VTrans Objectives/Approach
NodeLegs

## Slide 12
One Node is the Principal Node
A subset of the NodeLegs are Principal NodeLegs
VTrans Objectives/Approach
NodeLegs

## Slide 13
One Node is the Principal Node
A subset of the NodeLegs are Principal NodeLegs
VTrans Objectives/Approach

## Slide 14
Simple Intersections
    Single Node and its Legs
Complex Intersections
    Multiple Nodes and all their Legs
    Generalized to a single Node and one Leg per ‘approach’
Also → Nodes with NodeLegs, but Not Intersections:
    Dangles (one Leg, dead ends)
    Pseudonodes (two Legs, split polyline)
    Not-at-grade Nodes
    Transitions between single and dual carriageways
Nodes and Legs → Intersections
Notes: Easier to maintain ALL Nodes and NodeLegs than some.
Attributions clarifies which Nodes belong to intersections, and which represent complex intersections

## Slide 15
    Published “Safety Performance Functions” (SPFs) are based on safety statistics and real intersections
    Safety Analyst assumes intersection attributes are consistent with assumptions underlying each SPF
    Intersection Geometry and Stop Control assumed to be consistent with definitions of Major and Minor routes
    Major Route – Thru-route with more traffic
    Minor Route – Intersects Major route, has stop control
Safety Analyst’s Perspective
Notes: We had to make sure our data would be useful with Safety Analyst (not just compatible)
So a major (no pun intended) task was to understand the assumptions built into the SPFs and definitions of Major and Minor routes.

## Slide 16
Sort NodeLeg records in order of decreasing AADT!
Notes: It was easiest for me to develop a method of determining Major and Minor legs by finding patterns when the legs were listed in order of decreasing AATD (In this case ranking the Legs 1-4)

## Slide 20
Notes: Now… how to translate this to Major and Minor?

## Slide 21
How does knowing the rank of NodeLegs help us identify an intersection’s Major and Minor routes?
Which NodeLegs provide values for a Node’s attributes for Major and Minor routes?
How do we keep track of this in our data?
Leg Rank → Major & Minor?

## Slide 22
Major route attributes – Transferred from a Node’s “Major Leg” (highest AADT)
Minor route attributes – Transferred from a Node’s Leg with highest AADT that intersects the Major route
Leg Rank → Major & Minor?

## Slide 23
?
?
?
?
Notes: Now… how to translate this to Major and Minor?

## Slide 24
Notes: Here we have a view of a few intersections in Vermont’s capital city, Montpelier

## Slide 25
Notes: Here we have a view of a few intersections in Vermont’s capital city, Montpelier

## Slide 26
Notes: Here we have a view of a few intersections in Vermont’s capital city, Montpelier

## Slide 27
Notes: Once we know which legs are Major 1, Major 2, Minor 1, and Minor 2

## Slide 28
Notes: These NodeLegs that are ranked 1-4 have UniqueIDs (NodeLegID)

## Slide 29
Notes: Here we have a view of a few intersections in Vermont’s capital city, Montpelier

## Slide 30
Major 1 always highest AADT (except some T intersections)
Major 2 always cross-street of Major 1
    Major 2 = Leg 2 if Angle 1-2 ≈ 180°
    Major 2 = Leg 3 if Angle 1-2 ≈ 180°
Minor 1 is intersecting leg with highest AADT
Minor 2 is cross-street of Minor 1
How To “Automate”?
Notes: Most general consideration

## Slide 31
Notes: Here we have a view of a few intersections in Vermont’s capital city, Montpelier

## Slide 32
Query subset of Nodes that will have same relationship between Leg rank and Major/Minor designation
(Angle_1_3 >= 175 AND Angle_1_3 <= 185) AND (Angle_1_2 >= 75 AND Angle_1_2 <= 95) AND AADT_NullCount = 0
How To “Automate”?
(Look at Nodes where all
Legs have AADT values)

## Slide 33
Bulk populate Major_1, Major_2, etc. fields indicating Leg rank and corresponding NodeLegID
From previous query, Legs 1-4 (sorted by AADT) are:
    Major_1, Minor_1, Major_2, Minor_2 (respectively)
In other words:
    Major_1, Minor_1, Major_2, Minor_2 are Legs 1, 3, 2, 4
How To “Automate”?

## Slide 34
Notes: Here we have a view of a few intersections in Vermont’s capital city, Montpelier

## Slide 35
Notes: Here we have a view of a few intersections in Vermont’s capital city, Montpelier

## Slide 36
HMS Toolbar
  Node-centric tools – select intersecting Road Centerline arcs and (depending on tool) the Node its NodeLegs
      LegsOnly
      AddAll
      UpdateAll
      UpdateNodeLegCount
  Centerline-centric tools – select any number of Road Centerline arcs
      CheckRelationalAttributes
      CheckRoadwayAttributes
      UpdateRelationalAttributes
      UpdateRoadwayAttributes
ArcMap AddIns
Notes: I have documentation that describes (from an editor’s perspective) the tools and their use

## Slide 37
Before Road
Centerline
Edits
After Road
Centerline
Edits
After
Running
UpdateAll
ArcMap AddIns
UpdateAll Button
(attributes
too!)
Notes: Here we have a view of a few intersections in Vermont’s capital city, Montpelier

## Slide 38: Future Directions
Complex (or all!) Intersections in Tables
    Geometry of Intersections (points) and Approaches (lines) = geometry of Principal Nodes and Principal NodeLegs
    Attributes represent the entire intersection or approach direction
(Nodes and NodeLegs datasets reserved for feature-specific attributes)

## Slide 39: Future Directions
Maintain rules for summarizing Intersections (and complex approaches) within Table attributes
    Add AADT of dual carriageways
    Average Leg skew angles
    represent the entire intersection or approach direction

## Slide 40: Thanks! Questions?
VTrans Mapping Unit:
  Johnathan Croft
  Sara Moulton
  Michael Trunzo
Contact:
Kerry.Alley@vermont.gov